1. Read traverse size (n)
2. Read travers angles {a[i], i=0..n-1}
  1. For every angle {a[i], i=0..n-1}
  2. Read the angle (a[i])
3. Calculate the actual sum of the angles (sum)
  1. Initialize sum to zero (sum = 0)
  2. For every angle {a[i], i=0..n-1}
  3. Update the sum (sum = sum + a[i])
4. Calculate the correction
  1. The theoritical sum (tsum = 180 * (n – 2))
  2. The error (error = sum – tsum)
  3. The correction (correction = error / n)
5. Correct the angles
  1. For every angle {a[i], i=0..n-1}
  2. Correct the angle (a[i] = a[i] - correction)
6. Print the corrected angles
  1. For every angle {a[i], i=0..n-1}
  2. Print the angle (a[i])

Write a program that reads traverse angles a_1, a_2, \ldots, a_n , performs Traverse Angle Balancing, and prints the corrected angles {\^a}_1, {\^a}_2, \ldots, {\^a}_n .

\begin{align*} e&=\left (\sum \limits_{i=1}^{n}{a_i} \right )- 180(n-2)\\ c&=e/n\\ {\^a}_i&=a_i-c \forall i \in [1,n]\\ \end{align*}